3.6.1 Input / Output parameters
What is significant ? Why some parameters are fixed and others variable ?

Input
There are several groups of simulation parameters significant in performed experiments. However mostly the parameters regulating features characteristic of 802.11ah impact our findings.
First there are basic variables such as :
Nsta – the total number of client stations to be simulated
SimulationTime – the total duration of experiment,
BeaconInterval – time between sending consecutive beacon frames,
rho – the radius of circle area in which AP’s and station’s positions are distributed
randomly (normal distribution). Ap is in the centre of such circle. The result of this random placement changes with seed – parameter of RandomVariableStream.
There are also path parameters which specify the location of various config files (traffic and RAW configs).

Secondly there are Wi-Fi mode parameters, mainly DataRate, DataMode and bandWidth.
There is also possibility to employ rate control algorithms to set those automatically.

The last group of parameters is 802.11ah specific : RAW & TIM related. By default, RAW is fixed and based on OptimalRAW parameter set which specifies what and how often is sent in RPS message. This raw config file defines RPS values such as RPSs (RAW Parameter Sets) to be broadcasted with beacons in cycles (e.g. Beacon1: RPS1, Beacon2: RPS2, Beacon3: RPS1, Beacon4: RPS2, ...). It also specifies RAW grouping properties describing groups and slots.
Here configurable options are :
RawControl - Whether RAW can be accessed by any stations within the RAW group or only the paged stations within the RAW group,
CrossSlotBoundary - whether STAs are allowed to transmit after the assigned RAW slot boundary, SlotFormat – format of RAW slot count,
NRawSlotCount - Used to calculate number of RAW slot duration,
NRawSlotNum - number of slots per RAW group,
Page - page index of the subset of AIDs,
Aid_start/end- station with the lowest/highest AID allocated in the RAW

Output
There are several indicators of network performance measured in this work. First and the most obvious is average summary network throughput in saturation state. It will be further broken down into throughput of individual stations paired with analysis of their behavior through pcap and other trace files. The second value which will tell about convergence and connectivity effectiveness will be STA association time in first as well as station transmission latency in second stage. These will help to evaluate performance in consecutive thresholds of maximum number of connected nodes.